FU TEN DUO INDUSTRIAL CORP.

# Automatic Blow Molding machine/Double head, Single station

These machines are specially developed for high production of the products. It can product two or three cavities at one time and has automatic deflashing design. This will save man power and raise the economical benefits.

| Automatic Blow Molding machine/Double Head, Single Station. |
| --- |
| BASIC SPECIFICATION | Model NO. | FTD-645D | FTD-655D | FTD-665D |
|  | Material: | PP/PE, PVC | PP/PE, PVC | PP/PE, PVC |
|  | Product Min/Max Cap. | cc | 40~400 | 100~1000 | 200~1800 |
|  | Product Min/Max Dia. | mm | 20~70, 20~65 | 30~85, 30~80 | 40~100, 40~95 |
|  | Product Weight | g | 5~45, 5~30 | 10~70, 10~60 | 20~110, 20~100 |
|  | Extruding Mouth Outer Dia. | mm | 40 | 45 | 65 |
|  | Dry Cycle | Sec. | 3.4 | 3.6 | 3.8 |
|  | Max Extrusion Capacity | kg/hr | 22, 25x2 | 33, 38x2 | 45, 48x2 |
| EXTRUSION SYSTEM | Screw Diameter | mm | 45, 45x2 | 55, 55x2 | 65, 65x2 |
|  | L/D Ratio | L/D | 22/1 | 22/1 | 22/1 |
|  | Screw Rotating speed | r.p.m | 20~60, 20~50 | 20~60, 20~50 | 20~60, 20~50 |
|  | Extruding VS Motor | HP | 10, 15x2 | 15, 20x2 | 20, 25x2 |
|  | Number of Heaters | Zone | 6, 9 | 6, 9 | 6, 9 |
|  | Heating Capacity | KW | 11.5, 15 | 12, 21.5 | 15, 23 |
|  | Central distance of Twin-die head | mm | 110 | 130 | 150 |
| MOULD SYSTEM | Max/Min opening stroke | mm | 80~320 | 90~410 | 90~550 |
|  | Mould clamping force | Ton | 2.6 | 3.3 | 4.8 |
|  | Max. Mould Dimension | mm | 280x320 | 300x380 | 330x420 |
| HYDRAULIC SYSTEM | Hydraulic pump power | HP | 7.5 | 7.5 | 10 |
|  | Air Pressure | kg/cm² | 5~6 | 5~6 | 5~6 |
|  | Air compressor | HP | 5 | 5 | 7.5 |
|  | Oil tank capacity | Gallon | 70 | 90 | 110 |
|  | Electricity consumption | KW | 24.5, 47.5 | 32.5, 50.5 | 37.3, 63.9 |
| PACKING | Net weight | Ton | 3 | 3.5 | 4.2 |
|  | Machine size | M | 2.1x1.7x2.3 | 2.5x1.8x2.6 | 2.8x2.0x2.8 |
|  | Packing size | M | 2.2x1.8x2.1 | 2.6x1.9x2.4 | 2.9x2.1x2.6 |

All specification and design are subject to change without notice.